## Slide 1
新学術領域「宇宙の歴史をひもとく地下素粒子原子核研究」 2015年領域研究会
2015年5月15日-17日 神戸大学百年記念館 六甲ホール
嶋 達志
大阪大学核物理研究センター
地上における極低バックグラウンド測定の可能性

## Slide 2
Why do we need low-BG on the Earth’s surface?
What is the origin of BG on the Earth’s surface?
How low can BG on the Earth’s surface be?
Summary
Contents

## Slide 3
Example. 12C(a,g)16O
12C(a,g)16O reaction rate at kT ~300keV governs
stellar evolution and 12C/16O ratio after He-burning.
Nucleosynthesis via a- and s-processes
Mass threshold of Type-II SN
Astrophysical S-factor at Ecm = 300 keV (Buchmann 1996)
1. Why we need low-BG on the Earth’s surface?

## Slide 4
Tur, Heger, Austin, ApJ671, 821 (2007)
(Multiplier to Buchmann 1996)
Nucleosynthetic yields vs 12C(a,g)16O rate
s~25%

## Slide 5
EUROGAM
M. Assunção et al., Phys. Rev. C73, 055801 (2006)

## Slide 6
Status of 12C(a,g)16O Cross Section Data
s ~ 10-11 b @700keV
~ 10-17 b @300keV (Gamow window;T9=0.2)

## Slide 7
12C beam 100 mA on He-gas target (10 mm thick, 0.01 atm)
Ec.m.= 700 keV, s= 1 pb
Detection efficiency for g-rays; e = 0.01
Statistics (example)
= 1.5 [count/d] ; stat. error ~14%
for 100day meas. with S/N~1
10 [count/d] for 136Xe 2nbb@KamLAND-Zen
A. Gando et al., PRL110, 062502 (2013)

## Slide 8
Nuclear astrophysics experiments in underground
LUNA
Cockcroft-Walton, 400keV, p 500mA, a 250mA
135% HPGe with passive shield
Gran Sasso; 3800 m w.e. underground
--- Fm ~10-6×Fm on ground
T. Szȕcs et al., EPJ A44, 513 (2010)

## Slide 9
DIANA
Two accelerators;
Cockcroft-Walton < 400 keV, < 100 mA
Dynamitron < 3MeV, < 5 mA
DUSEL (Homestake); 3800 m w.e. underground
--- Fm ~10-6×Fm on ground

## Slide 10
Hmm… “standard” is the “standard”.
But…
Underground accelerator is the
“standard tactics” of low-background
experiments on nuclear and particle
physics.

## Slide 11
125Sb(n,g)126Sb @30keV
s=0.3b (ENDF/B-VI)
0.6b (JENDL-4.0)
Neutron capture on unstable nuclei

## Slide 12
s(30keV)= 0.3b (ENDF/B-VI), 0.6b (JENDL-4.0)
125Sb T1/2 =2.76y
Accumulate 108 /s 125Sb for 7days ⇒ ~6×1013 of 125Sb
⇒ 126Sb production rate ~0.02 /s (Fn =109 n/cm2/s)
⇔ 125Sb decay rate ~5×105 /s
125Sb b- Qb=621.9keV
g 427.9keV 463.4keV 600.6keV 635.95keV (single)
126Sb b- Qb=1920keV
g 414.7keV 666.5keV 695.0keV (cascade, BR=83.3%)
Triple g-ray coincidence with multi-detector

## Slide 13
Osaka
(sea level, w/o Rn rejection)
Kamioka
(1000m underground, 2700m w.e.）
B: not shielded S: shielded (15cm OFHC+15cm Pb)
G: shielded, with Rn rejection
A: anti-coincidence with NaI C: coincidence with NaI
for 76Se 2+ → 0+ (559keV)
Ordinary
“Low-BG”
Detector
~1/1000
~10-3 /keV/hr
@2.5MeV
2. What is the origin of BG on the Earth’s surface?

## Slide 14
ELEGANT-III (171cc Ge + 4p anti-Compton NaI(Tl))
(Cross-sectional view) (Central part)
HPGe
Hg
OFHC
Pb
NaI
Air-tight Box
Liq.N2
N. Kamikubota et al., NIM A245, 379 (1986)

## Slide 15
HPGe (137%)
LUNA @Gran Sasso (3800 m w.e.)
Beam
10-3~10-4 /keV/hr @2.5MeV
--- comparable to ELEGANT-III

## Slide 16
Above 2.7MeV ;
Osaka
Kamioka
Fm (Kamioka) ~10-5 × Fm (Osaka)
208Pb 3-→0+ 2.615MeV is the g-ray
with highest energy from natural RIs.
BG(Kamioka) ~10-1 ×BG(Osaka)
- - - ~10% of BG(Osaka) is not due to cosmic rays
but due to a, b+g or neutrons from U, Th ?

## Slide 17
Experiments | Neutrino source | Signal | Significance
LSND | m Decay-At-Rest | nm  ne | 3.8s
MiniBooNE | p Decay-In-Flight | nm  ne | 3.4s
 |  | nm  ne | 2.8s
 |  | Combined | 3.8s
Ga (calibration) | e capture | ne  nx | 2.7s
Reactors | Beta decay | ne  nx | 3.0s
3. How low can BG on the Earth’s surface be?
Short-baseline n-osc. experiments; sterile?

## Slide 18
JSNS2
J-PARC Sterile Neutrino Search using ns
from J-PARC Spallation Neutron Source (E56)
M. Harada et al, arXiv:1310.1437 [physics.ins-det]

## Slide 19
Detector
Gd-loaded Liq. Scintillator or water Cherenkov, 25ton × 2,
detecting
(253000b@thermal)
te=1~10ms, Ee=20~60MeV
tg=1~100ms, Eg=6~12MeV
→ Delayed coincidence

## Slide 20
Main scintillators; (provided by
RCNP/LEPS2)
  24 scintillators in total. (~500kg)
  4 scintillators / layer and 6 layers
  2 Narrower (central part)
  2 Wider (in edge sides)
  Each scintillator has 4 PMTs, and 2 PMTs / one side
Inner cosmic veto (yellow)
  4.3cm thick PL scintillators
  One side readout.
  Rejection Efficiency >~99.5%
Outer cosmic veto (blue)
  PLs are used to surround main part.
  Size; 1m x 1m or 1m x 2.3m,
  1cm (t)
~3.5m
~1.5m
~1.0m
500kg detector for BG study
>99.8% (total)

## Slide 21
157Gd+n
Delayed g
Fast neutron
p
m
Prompt e
Beam-related background
No difference between
the prompt spectrum
(tp=1.75~4.65ms)
and the delayed spectrum
(td =tp +20ms).
Excess rate <2.1×10-7
[events/spill/300kW, 90%CL]
*Pulse interval of MLF is 40ms.

## Slide 22
Capture-g from
spallation target
Cosmic neutron or g
Beam-unrelated background
★ Beam neutron is negligible because
of no difference between prompt
and delayed signal rates.
S. Ajimura et al., to be appeared in PTEP, doi; 10.1093/ptep/ptv078

## Slide 23: PICO-LONのための超高純度NaI開発
NaI(Tl)結晶の純度(単位 μBq/kg)
結晶の純度はよくなった

## Slide 24: 全体のバックグラウンド （神岡地下で測定）
目標の20～30倍
殆どはNaI(Tl)周辺の素材に起因
Takemoto, Kozlov, Ikada, Teraoka

## Slide 25
NaI(Tl)
SiO2 Light Guide
NaI(Tl)結晶の仕様
  直径 ５インチ(127.0 mm)
  高さ ５インチ(127.0 mm)
PMTの仕様
  直径 ４インチ(102 mm)

## Slide 26
4. Summary
Low-BG detectors on the ground are useful for
accelerator experiments as well as non-acc.
experiments.
BG in higher energy region will be due to
cosmic-ray induced g, n
a, b+g, n from U, Th
- - - Are they reduced with additional shielding ?
Neutron generation by m-capture in Pb ?
Further purifications should be effective...
* K X-rays of muonic U, Th ~6MeV